## Slide 1: Shortest Path Based Geographical Routing Algorithm in Wireless Sensor Network
Indrajit Banerjee
Tuhina Samanta, Biswarup Das Sarma, Ahana Roy Choudhury, and Indrani Roy
Bengal Engineering and Science University, Shibpur

## Slide 2: Outline
Introduction
Problem definition
Proposed Algorithm
Performance Analysis
Conclusion
Reference

## Slide 3: Introduction
Sensor network is a collection of hundreds and thousands of low-cost, low power miniaturized electronic programmable devices
The nodes are deployed in a monitoring area
These devices are capable for
  data sensing of monitoring environment
  data processing
  communicating between each other

## Slide 4: Introduction
Monitoring Environment
Sensor node
Base Station

## Slide 5: Application of WSN
Low cost and effortlessly deployable nodes makes sensor network an attractive solution for a plethora of applications in various filed.
        Area monitoring
        Environmental/Earth monitoring
        Forest fire detection
        Air pollution monitoring
        Landslide detection
        Industrial monitoring
        Machine health monitoring
        Agriculture
        Greenhouse monitoring
        Structural monitoring

## Slide 6: Challenging Issues in WSN
Energy Optimization
Data Routing Problem
Fault Detection and Recovery
Obstacles Detection
Job Scheduling
Coverage Problem
Localization Problem

## Slide 7: Data Routing Problem in WSN
There are many nodes deployed over an area. Now it is to be decided that which node the packet of data is to be forwarded to.
The route should be chosen in a way that the energy loss of a node should be minimum.
The number of hops should be minimum.
BS

## Slide 8: Data Routing Problem in WSN
The network performance to be maximised.
The data routing procedure must be efficient and also reliable.
The dead-loop problem must be addressed.
BS
BS

## Slide 9: Data Routing Problem in WSN
SOURCE
DESTINATION

## Slide 10: Data Routing Problem in WSN
SOURCE
DESTINATION

## Slide 11: Data Routing Problem in WSN
SOURCE
DESTINATION
There are 3 paths between SOURCE and DESTINATION. Which to choose???

## Slide 12: Design Paradigm
Proposed algorithm is a heuristic approach based data routing scheme which tries to find the shortest possible path between two nodes
Salient features of the proposed work are
  Use of simple Euclidean geometry to decide the path in which the data packets are to be forwarded
  Decrease in data delivery delay with increase in number of nodes
  Decrease in data delivery overhead

## Slide 13: Presenting our Algorithm

## Slide 14: Our Algorithm
SOURCE
DESTINATION

## Slide 15: Our Algorithm
SOURCE
DESTINATION

## Slide 16: Experimental Result
The algorithm was implemented using C programming language.
We have considered that each of the nodes has a range of 250 meters as in RGRP [2].
The source node and the destination node are selected randomly over the layout, between which connection is established.
We took average on 50 different execution results.

## Slide 17: Experimental Result
Simulated network topology characteristics
In our simulation we are gradually increasing the node number from 5 to 50. The transmission rate is also increased from 2kbps to 512kbps and also the data size is increased from 64 bytes to 1000 bytes. The simulation details are elaborated in the given Table.
Nodes | Region | Data Size | Transmit Rate
5 | 800m*800m | 64 bytes | 2Kbps
10 | 800m*800m | 250 bytes | 128Kbps
15 | 800m*800m | 250 bytes | 128Kbps
20 | 1000m*1000m | 1000 bytes | 512Kbps
25 | 1000m*1000m | 1000 bytes | 512Kbps
50 | 1000m*1000m | 1000 bytes | 512Kbps

## Slide 18: Experimental Result
Delay metric
As the total number of nodes in a deployed region is increased, delay in the network is increased irrespective of the increased data rate. However, our algorithm outperforms some of the existing algorithms in terms delay metric.
Average end-to-end delay vs. number of node

## Slide 19: Experimental Result
Average end-to-end delay vs. number of node
We see that our algorithm’s performance is similar to RGRP for smaller number of nodes and when number of nodes is 13-15 delay in our algorithm is slightly more. With the increase in number of nodes our algorithm performs better than both RGRP and GPSR. As our proposed method is capable of completing data transfer from source to the destination node with minimal number of hops, end-to-end delay is reduced.

## Slide 20: Experimental Result
Number of Nodes | Delay considering data size of 64 bytes and rate of 2kbps | Delay considering data size of 250 byte and rate of 120 kbps | Delay considering data size of 1000 bytes and rate of 512 kbps
5 | 0.015 | 0.25 | 0.25
10 | 0.015 | 0.25 | 0.25
15 | 0.015 | 0.25 | 0.25
20 | 0.022 | 0.367 | 0.367
25 | 0.027 | 0.45 | 0.45
30 | 0.027 | 0.45 | 0.45
35 | 0.028 | 0.475 | 0.475
40 | 0.029 | 0.487 | 0.487
45 | 0.027 | 0.45 | 0.45
50 | 0.028 | 0.462 | 0.463
Delay calculation for different data size and data rate
The delay is in seconds.

## Slide 21: Experimental Result
Number of Nodes | Our Algorithm | RGRP | GPSR (b=5.0)
5 | 0.25 | 0.25 | 0.5
10 | 0.25 | 0.25 | 0.5
15 | 0.15 | 0.15 | 0.3
20 | 0.22 | 0.525 | 0.675
25 | 0.27 | 0.525 | 0.48
30 | 0.27 | 0.675 | 0.675
35 | 0.285 | 0.81 | 0.825
40 | 0.295 | 0.96 | 1.05
45 | 0.27 | 1.05 | 1.2
50 | 0.2775 | 1.2 | 1.35
Delay calculation and comparison with some existing algorithms
The delay is in seconds.

## Slide 22: Experimental Result
Number of Nodes | Our Algorithm | RGRP | GPSR (b=5.0)
5 | 0.25 | 0.25 | 0.5
10 | 0.25 | 0.25 | 0.5
15 | 0.15 | 0.15 | 0.3
20 | 0.22 | 0.525 | 0.675
25 | 0.27 | 0.525 | 0.48
30 | 0.27 | 0.675 | 0.675
35 | 0.285 | 0.81 | 0.825
40 | 0.295 | 0.96 | 1.05
45 | 0.27 | 1.05 | 1.2
50 | 0.2775 | 1.2 | 1.35
Delay calculation and comparison with some existing algorithms

## Slide 23: Experimental Result
Overhead metric
The given Table represents average routing overhead in our algorithm. Each time a possible active node is chosen for data transfer from the nearest neighbor in the coverage area, data from the present selected node is transferred to them for finding the distance vector, hence adding a new overhead. Average routing overhead is calculating by taking the average of the neighbor nodes in each iteration.
Number of Nodes | Our Algorithm | RGRP | GPSR (b=5.0) | GPSR (b=2.5)
5 | 2 | 0 | 90 | 175
10 | 3 | 50 | 175 | 280
15 | 5 | 60 | 200 | 400
20 | 5 | 70 | 230 | 500
25 | 7 | 80 | 380 | 690
30 | 8 | 80 | 420 | 800
35 | 8 | 70 | 500 | 900
40 | 9 | 70 | 580 | 1000
45 | 9 | 60 | 590 | 1100
50 | 11 | 50 | 600 | 1200
The overhead is in terms of number of packets.
Overhead calculation

## Slide 24: What We Have Achieved
The proposed algorithm has utilized simple Euclidean geometric rules to find an optimum routing path.
The main idea is to choose a routing path that is very near to the straight line path between the source and destination node.
In a heavily deployed environment, the delay is much lesser than the existing algorithms.
The overhead is also considerably lesser.
The dead-loop problem can be avoided very easily.

## Slide 25: References
Junlong Lin, Geng Sheng Kuo, “A Novel Location-fault-tolerant Geographic Routing Scheme for Wireless Ad Hoc Networks”, 63rd IEEE Vehicular Technology Conference, 7-10 May 2006, pp.1092 – 1096.
Rong Ding; Lei Yang, "A Reactive Geographic Routing Protocol for Wireless Sensor Networks", Sixth International Conference on Intelligent Sensors, Sensor Networks, and Information Processing(ISSNIP), Beijing, China, 2010 IEEE, pp. 31 - 36.
Sundar Subramanian, Sanjay Shakkottai and Piyush Gupta, "On Optimal Geographic Routing in Wireless Networks with Holes and Non-Uniform Traffic", 26th IEEE International Conference on Computer Communications, INFOCOM 2007, pp. 1019 - 1027.
Sundar Subramanian and Sanjay Shakkottai, "Geographic Routing with Limited Information in Sensor Networks", IEEE Transactions on Information Theory, Volume 56, Issue 9, September, 2010 pp. 4506-4519.
Ivan Stojmenovic, "Position-based Routing in Ad Hoc Networks," IEEE Communications Magazine, vol. 40, July 2002, pp. 128-134.
Hannes Frey, "Scalable Geographic Routing Algorithms for Wireless AdHoc Networks", IEEE Network, vol. 18, July-Aug. 2004, pp. 18-22.
Brad Karp and H. T. Kung, "GPSR: Greedy Perimeter Stateless Routing for Wireless Networks," Proc. of the ACM/IEEE International Conference on Mobile Computing and Networking, Aug. 2000, pp. 243-254
Fabian Kuhn, "Geometric Ad-hoc Routing: of Theory and Practice", Proc. of the Twenty-second Annual Symposium on Principles of Distributed Computing, July 2003, pp. 63-72.
Rajagopal Iyengar and Biplab Sikdar, "Scalable and Distributed GPS Free Positioning for Sensor Networks," Proc. of ICC 2003, vol. 1, May 2003, pp.338-342.
Dragos Niculescu and Badri Nath, "Ad Hoc Positioning System (APS) using AOA" Proc. of INFOCOM 2003, Vol. 3, April 2003, pp. 1734-1743.

## Slide 26: References
Niveditha Sundaram and Parameswaran Ramanathan, "Connectivity Based Location Estimation Scheme for Wireless Ad Hoc Networks", Proc. of IEEE GLOBECOM 2002, Vol. 1, Nov. 2002, pp. 143-147.
A. Rao, C. Papadimitriou, S. Shenker and I. Stoica, "Geographic Routing without Location Information", Proc. of the 9th annual international conference on Mobile Computing and Networking, 2003, pp. 96-108.
G. Finn, “Routing and addressing problems in large metropolitan scale internetworks,” ISI Research Report ISI/RR-87-180, University of Southern California, March 1987.
P. Bose, P. Morin, I. Stojmenovic, and J. Urrutia, “Routing with guaranteed delivery in ad hoc wireless networks,” ACM Wireless Networks, vol. 7, no. 6, Nov. 2001, pp. 609 – 616.
S. Giordano, I. Stojmenovic, and L. Blazevic, “Position based routing algorithms for ad hoc networks: a taxonomy,” Ad Hoc Wireless Networking, X. Cheng, D. Z. Du, and X. Huang (eds.), Kluwer, 2004, pp.103–136.
N. Carlsson and D. L. Eager, “Non-Euclidian geographic routing in wireless networks”, Ad Hoc Networks, Vol. 5, no. 7, September 2007, pp. 1173–1193.
S. Lee, B. Bhattacharjee, and S. Banerjee, “Efficient geographic routing in multihop wireless networks”, Proc. MobiCom, New York, NY, May 2005, pp. 230-241.
M. Zuniga, K. Seada, B. Krishnamachari, and A. Helmy, “Efficient geographic routing over lossy links in wireless sensor networks”, ACM Transactions on Sensor Networks, Vol. 4, no. 3, May 2008, pp. 1–33.
V. Kranakis, H. Singh, and J. Urrutia, “Compass routing on geometric networks”, Proc. Canadian Conference on Computational Geometry ’99, Vancouver, Canada, Aug. 1999, pp. 51-54.
I. F. Akyildiz, W. Su, Y. Sankarasubramaniam, and E. Cayirci, "A survey on sensor networks", IEEE Communications Magazine, August 2002, pp.102–116.

## Slide 27: References
D. Estrin, J. Heidemann, R. Govindan, and S. Kumar, "Next century challenges: Scalable coordination in sensor networks", Proceedings of ACM Mobicom, Seattle, WA, August 1999, pp. 263-270.
K. Sohrabi, J. Gao, V. Ailawadhi, and G.J. Pottie, "Protocols for selforganization of a wireless sensor network", IEEE Personal Communications, October 2000, pp.16–27.
Indrajit Banerjee Hafizur Rahaman and Biplab K Sikdar, “UDDN: Unidirectional Data Dissemination via Negotiation”, IEEE Conference on Information Networking, ICOIN 08., 23-25 Jan. 2008, pp. 1 – 5.
Indrajit Banerjee, Prasenjit Chanak, Biplab Kumar Sikdar, Hafizur Rahaman, “EERIH: Energy Efficient Routing via Information Highway in Sensor Network”, IEEE International Conference on Emerging Trends in Electrical and Computer Technology - ICETECT, 2011, pp.1057-1062.
Indrajit Banerjee, Prasenjit Chanak, Biplab Kumar Sikdar, Hafizur Rahaman, “EER: Energy Efficient Routing in Wireless Sensor Networks by Department of Information Technology”, Proceeding of the 2011 IEEE Students' Technology Symposium 14-16 January, 2011, IIT Kharagpur, pp. 92-97.
B. Karp and H. T. Kung, “GPSR: greedy perimeter stateless routing for wireless networks,” in Proc. MobiCom ’00, New York, NY, Aug. 2000

## Slide 28
Thank You